## Slide 1
HARAM SAFE
Reliable Crowd Management for Masjid al-Haram

## Slide 2
  Hajj 1445H (2024): 1,833,164 pilgrims
  Hajj 1446H (2025): 1,673,230 pilgrims
current scale :
Why crowd reliability at the Haram matters
  Each year Haram hosts millions of pilgrims from around the word during Hajj/Ramadan
  Any small delays in response , human error , can escalate to a catastrophic failure, System Failure , that can cost human lives
  To design a reliable systems means that the system would still work under sensor loss , link failure , or operator overload.
  Our approach to the system is applying : Fault avoidance , Fault detection , and Fault detection

## Slide 3
  Green ≤ 4 people/m²
  Red ≥ 6 people/m²
  Crowd Threshold
Hazards & Reliability Targets
  Availability ≥ 99.99% (peak hours);
  POFOD ≤ 1×10⁻⁵ per safety demand;
  ROCOF false-red ≤ 1 per 12 h
  Reliability Goals
  Heat surges
  Dangerous density
  Evacuation impediments
  Natural Hazards
  Digital outages
  Alert fatigue
  some
  Tech Hazards

## Slide 4
  Data collection : CCTV computer vision, overhead thermal counters, BLE/Wi-Fi , manual clickers.
  Data transport : 5G + fiber , QOS
  Self-monitoring analytics :
    Channel A : CV model 1 (vendor + backbone)
    Channel B: CV model 2 (another vendor + backbone)
    comparing : flags mismatch > over N frames > conservative fallback
  Protection service : watches density/derivative/heat; commands issues Close/Reroute/One-Way directly to field controllers
  Operators UI : Bilingual console + playbook, manual override
  Actuators : screen dynamic signage, barriers, gates, misting, water dispatch
System Architecture

## Slide 5
Reliability patterns
  Protection System (simple, diverse, independent): enforces thresholds and executes actions with very low POFOD.
  Self-Monitoring (multi-channel): two heterogeneous models + comparator; on mismatch → safe-side fallback.
  Active-Active High Availability: two monitoring stacks; failover without operator action.
  Time-bounded calls (timeouts) to all external services; bounded queues; idempotent commands to actuators.
  Data diversity: thermal + vision + presence reduce single-modality bias.

## Slide 6
Fault tree + coding guidelines
  Top event: crowd crush in zone Z
  Trigger: density ≥ 6 p/m² for ≥ 30 s
  Late response: action > 90 s after first red
  Why density rises: inflow spike · bottleneck · counter-flow · obstacle
  Why action is late: sensor/analytics down · operator overload · command path fail · physical jam
  What we do: one-way routing + obstacle control; independent protection sends Close/Reroute with timeout+ retry
  Encapsulate config (no globals)
  Validate every input (range/format)
  Handle all exceptions
  Avoid shared mutables / FP equality
  Safe restart & resume (recover state)
  Bounds checks on arrays/queues
  Timeouts on I/O/actuation (≈2 s try)
  Named constants (no magic numbers)

## Slide 7
Testing like the real world
  Operational profiles (weights): Evening Umrah (0.35), Friday prayers (0.15), Ramadan(0.20), Hajj peak windows (0.20), Off-peak (0.10).
  Scenario drills: sudden gate closure, enforce one-way flows, create ambulance corridor (< 90 s).
  Chaos tests (off hours): drop camera feed, fail one 5G link, crash one model—protection must still act.
  Human-in-the-loop: bilingual UI usability and alert fatigue checks.

## Slide 8
How we measure and prove reliability
  Availability (AVAIL) per peak hour, POFOD for safety actions, ROCOF for false-reds, p95 detection latency.
  Prototype simulation (discrete time): arrivals → Mataf density → thresholds → measure AVAIL & POFOD with injected failures.
  Observed (illustrative run): Availability ~96.9%, POFOD ~4.0% → needs higher MTBF, lower MTTR, and parallel stacks to reach targets.
  Path to targets: 2 active-active stacks (independent) + auto-failover + faster repair → hour-level AVAIL ≥ 99.99%; tiny protection service to push POFOD ≤ 1e-5.

## Slide 9
Vision 2030 & Future
Artificial Intelligence (AI)
Ethics
Scalability
  Dual CV channels + comparator
  Predictive reroute suggestions
  PDPL by design: counts/heatmaps only
  Edge blurring, short retention, audit trails
  Digital twin; 5G slicing + fiber ring
  Metro/train integration; active-active DC

## Slide 10
THANK YOU